## Slide 1
5th International Seminar on
ORC Power Systems
Athens Greece
ULTRA-LOW GWP REFRIGERANT MIXTURES AS WORKING FLUIDS IN ORC FOR WASTE HEAT RECOVERY
Athens, 09 September 2019
Konstantinos Braimakis*, Angelos Mikelis, Antonios Charalampidis
and Sotirios Karellas
National Technical University of Athens (NTUA)

## Slide 2: Contents
Motivation
Methodology
Results and discussion
Conclusions

## Slide 3: Motivation
F-gases regulation and the need for ultra-low GWP refrigerants
EU: Restrictions and bans on refrigerants with GWP>150
Aim: reduction of fluorinated gases by two-thirds compared to 2014
Search for new, ultra-low GWP (<150) refrigerants
Natural hydrocarbons and hydrofluoroolefins (HFOs)
ORCs with zeotropic fluids (ZORCs): efficiency improvement strategy
Goal of present work:
Efficiency improvement potential of ZORCs running with ultra-low GWP fluids

## Slide 4: Motivation
The use of zeotropic fluids as-gases regulation and the need for ultra-low GWP refrigerants
glide
glide
ηhsu increase

## Slide 5: Motivation
The use of zeotropic fluids as-gases regulation and the need for ultra-low GWP refrigerants
Glide in evaporation
pinch point in evaporator
pinch point in preheater
Glide in condensation
pure fluid
mixture
PPcond
PPheat
PPheat
T
PPcond
Tcw,in
ΔΤcw,cond
cooling water
Ths,out
T
PPheat
heat
QORC,in,2
QORC,in,1
heat source stream
mixture
pure fluid
Ths,out
ηhsu increase

## Slide 6: Methodology
Standard ORC layout
7 working fluids: 3 HCs, 2 HFOs, CO2 and 1 HFC
Working fluid | pcr (bara) | Tcr (°C) | ODP | GWP | Type
n-pentane (R601) | 33.7 | 196.6 | 0 | 4 | HC
Isobutane (R600a) | 36.5 | 134.7 | 0 | 3 | HC
propylene (R1270) | 46.2 | 91.9 | 0 | 1.8 | HC
R1234ze(E) | 33.4 | 109.4 | 0 | 6 | HFO
R1234yf | 33.8 | 94.7 | 0 | 4 | HFO
CO2 (R744) | 73.8 | 31.0 | 0 | 1 | –
R32 (R-410a repl.) | 57.8 | 78.1 | 0 | 675 | HFC
Concentration ratios ranging from 10/90 to 90/10
Evaporation pressures: 2 to 42 bar, increments of 4 bar
Examined heat source temperatures : 100-300 °C, increments of 10 K
AspenPlusTM model, PR-BM Property method

## Slide 7: Methodology
2 optimization variables
pevap
Goal: maximization
ηex
C
Parameter | Value
Expander isentropic efficiency (–) | 0.75
Pump isentropic efficiency (–) | 0.80
Pump motor isentropic efficiency (–) | 0.85
Generator efficiency (–) | 0.95
Cooling water inlet temperature (°C) | 20
Cooling water temperature increase (K) | 15
Evaporator pinch point (K) | 10
Condenser pinch point (K) | 10
Maximum superheating (K) | 10
AspenPlusTM flowsheet

## Slide 8: Results and discussion
Pure fluid ORCs
Zeotropic ORCs
Maximum exergetic efficiency of optimised cycles
PORCs: n-pentane most favourable for T>200 °C, R1234yf, R1234ze(E) and isobutane favourable successively at lower temperatures
ZORCs: n-pentane mixtures superior throughout whole temperature range followed by isobutane, R1234ze(E) and R1234yf mixtures
R32 exhibits lowest performance in both configurations
CO2 does not lead to feasible PORC within examined temperature range

## Slide 9: Results and discussion
Maximum exergetic efficiency of optimised cycles
Ths ( °C) | ZORCs |  |  |  | PORCs |  | 
 | ηex (%) | Working fluid | Copt | pev (bar) | ηex (%) | Working fluid | pev (bar)
100 | 2.66 | n-pentane/isobutane | 0.4/0.6 | 6 | 1.64 | isobutane | 10
120 | 4.39 | n-pentane/isobutane | 0.6/0.4 | 6 | 3.14 | isobutane | 14
140 | 6.48 | n-pentane/isobutane | 0.3/0.7 | 10 | 5.36 | R1234ze(E) | 26
160 | 9.19 | n-pentane/R1234ze(E) | 0.1/0.9 | 30 | 7.86 | R1234ze(E) | 34
180 | 12.11 | n-pentane/R1234ze(E) | 0.2/0.8 | 34 | 10.91 | isobutane | 30
200 | 14.99 | n-pentane/isobutane | 0.2/0.8 | 30 | 13.11 | isobutane | 34
220 | 17.40 | n-pentane/isobutane | 0.3/0.7 | 30 | 15.77 | n-pentane | 14
240 | 20.05 | n-pentane/isobutane | 0.8/0.2 | 26 | 19.14 | n-pentane | 18
260 | 22.03 | n-pentane/isobutane | 0.8/0.2 | 30 | 21.55 | n-pentane | 26
280 | 23.05 | n-pentane/R1234ze(E) | 0.9/0.1 | 30 | 22.88 | n-pentane | 30
300 | 23.46 | n-pentane/isobutane | 0.9/0.1 | 30 | 23.48 | n-pentane | 30
n-pentane/isobutane mixtures favourable over along range of temperatures

## Slide 10: Results and discussion
Relative exergetic efficiency difference optimised PORCs vs ZORCs

## Slide 11: Results and discussion

## Slide 12: Results and discussion
ZORCs more beneficial at low Ths
Low potential for Ths>150-180°C
PORCs superior to ZORCs at higher temperatures
Highly variable rel. exergetic eff. increase: can be up to 63% for examined fluids

## Slide 13: Results and discussion
 | R1234ze(E) | propylene | isobutane | n-pentane | CO2
R1234yf | 2.97% 140℃ | 1.94% 100℃ | 9.20% 100℃ | 51.26% 100℃ | 34.05% 100℃
R1234ze(E) | - | 10.29% 100℃ | 3.90% 120℃ | 62.92% 100℃ | 35.61% 100℃
propylene | - | - | 30.83% 100℃ | 49.52% 100℃ | 36.56% 100℃
isobutane | - | - | - | 62.44% 100℃ | no benefit
n-pentane | - | - | - | - | no benefit
Maximum relative exergetic efficiency increase for different mixtures
Maximum relative exergetic efficiency difference of each ZORC and the PORCs
running with its mixture components

## Slide 14: Results and discussion
relative exergetic efficiency difference
I
II
III
IV
Tcrit,LTC
Tcrit,HTC
V
LTC fluid PORC
ηex maximization
HTC fluid PORC
ηex maximization
HTC molar concentration
evaporation pressure
heat source temperature
ZORC vs. PORC comparison: General pattern

## Slide 15: Results and discussion
relative exergetic efficiency difference
I
II
III
IV
Tcrit,LTC
Tcrit,HTC
V
LTC fluid PORC
ηex maximization
HTC fluid PORC
ηex maximization
HTC molar concentration
evaporation pressure
heat source temperature
ZORC vs. PORC comparison: General pattern
PORC>ZORC
PORC>ZORC

## Slide 16: Results and discussion
relative exergetic efficiency difference
I
II
III
IV
Tcrit,LTC
Tcrit,HTC
V
LTC fluid PORC
ηex maximization
HTC fluid PORC
ηex maximization
HTC molar concentration
evaporation pressure
heat source temperature
ZORC vs. PORC comparison: General pattern
Optimized latent/sensible heat ratio and glide in condenser
Glide in evaporator predominant
ZORC>PORC
ZORC>PORC

## Slide 17: Conclusions
ZORCs can lead to relative exergetic efficiency increase to up to 60 %
compared to PORCs (commonly 20-40%)
Efficiency benefits occur at heat source temperatures lower than 150-180 °C
Dramatic efficiency increase at 100-120 °C
n-pentane/isobutane mixtures favourable under a wide range of
heat source temperatures
For each combination of fluids, ZORCs are superior to PORCs when Ths<Tcrit,LTC
and Tcrit,LTC<Ths<Tcrit,HTC
ZORCs possible replacements to PORCs which cannot be implemented due
to working fluid unavailability

## Slide 18: Conclusions
Thank you!
Contact info:
Dr. –Ing Konstantinos Braimakis
Email: mpraim@central.ntua.gr
Laboratory of Steam Boilers and Thermal Plants,
School of Mechanical Engineering,
National Technical University of Athens, Greece