## Slide 1
Seoul National University, South Korea
Hong Wone Choi, Jin Young Park, Dong Kyu Kim, Min Soo Kim
9 September 2019
Off-Design Analysis of Organic Rankine Cycle Integrated with Proton Exchange Membrane Fuel Cell (PEMFC)
5th International Seminar on ORC Power Systems, Athens Greece, 9-11 September 2019

## Slide 2: Overview
Backgrounds and Objective
Thermal Management for PEMFC
PEMFC-ORC Hybrid Power System
Conclusions
Results and Discussions

## Slide 3: Conventional Waste Heat Recovery (WHR) Applications
Reference
Bertrand F. et al., 2011, Renewable and Sustainable Energy Reviews, 15: 3963-3979
E. Macchi and M. Astolfi, 2017, Woodhead Publishing, pp. 613-627
Backgrounds and Objective
Low evaporation temperature and pressure
Less heat is needed during evaporation
High stability regardless of part-load / off-design operation
ORC is practical solution for enhancing energy efficiency
Industrial plant
Marine engine
Gas turbine
Diesel engine
Superheating is not essential

## Slide 4: Proton Exchange Membrane Fuel Cell (PEMFC)
Environment-friendly
Infinite fuel resource (H2)
Few moving parts and silent
High fuel cost (H2)
Efficiency degradation as electric load increases
Pros
Cons
Need to increase energy efficiency
Backgrounds and Objective

## Slide 5
TH
TC
QH
QC
Correlation of temperature and waste heat
Off-design characteristics
Optimal temperature
Objective
Stack
0
The bottoming ORC
Expander
Refrigerant
Pump
Evaporator
Condenser
The topping fuel cell
Gear Pump
Influence of Heat Source Condition
Backgrounds and Objective

## Slide 6
Reference
Choi et al., 2018, International Journal of Hydrogen Energy, 43: 13406-13419
Operating condition & PEMFC design
Fig. A cross-section view of single-cell PEMFC
Steady-state regime
Even temperature on membrane
Tout,fc = Tcell
Tout,fc – Tin,fc = 6 K
Tout,fc =298 K
Relative humidity: ϕH2,in= ϕair,in= 100%
Assumption
Parameter | Symbol | Value | Unit
Cell temperature | Tcell | 343~363 | K
Current density | jcell | 0.7~1.0 | A/cm2
Number of cell | Ncell | 50 | EA
Cell’s area | Acell | 200 | cm2
PEMFC Operating Condition
Thermal Management for PEMFC

## Slide 7
Activation voltage loss
Ohmic voltage loss
Concentration voltage loss
Cell voltage
Reversible voltage
Waste
heat
  Cell voltage (V)
  Current density (A/cm2)
Power
Fuel cell stack power
Electrochemical Theory for PEMFC Modeling
Thermal Management for PEMFC
Reference
R. O’hayre et al., 2016, John Wiley & Sons, pp. 77-200

## Slide 8
Energy conservation
Reference
X. Zhao et al., 2015, International Journal of Hydrogen Energy, 40: 3048-3056
Mass conservation
Thermal Management System Modeling
Thermal Management for PEMFC

## Slide 9
Fig. Schematic diagram for the hybrid power system
Methodology
PEMFC-ORC Hybrid Power System

## Slide 10
Receiver
Refrigerant
Pump
Evaporator
Condenser
Chiller
Expander
Fig. Description for the bottoming ORC system
Operating condition & ORC system design
Steady-state regime
Degree of subcooling (DSC) = 10 K
Assumption
Parameter | Symbol | Value | Unit
Mass flow rate of system | morc | 0.01~0.04 | kg/s
Mass flow rate of heat sink | msink | 0.35 | kg/s
Temperature of heat sink | Tsink | 298 | K
Number of plate of evaporator | Nevap | 32 | EA
Heat transfer area of evaporator | Aevap | 780 | cm2
Number of plate of condenser | Ncond | 50 | EA
Heat transfer area of condenser | Acond | 471 | cm2
ORC Operating Condition
PEMFC-ORC Hybrid Power System

## Slide 11
Heat exchanger
Brazed Plate Heat Exchanger (BPHE)
Expander
Pump
For counter-flow arrangement
Single-phase heat transfer
Evaporation
(Desideri et al., 2017)
(Yan et al., 1999)
Condensation
Two-phase heat transfer
Reference
A. Desideri et al., 2017, International journal of heat and mass transfer, 113: 6-21
Y. Y. Yan et al., 1999, International journal of heat an mass transfer, 42: 993-1006
A. Muley et al., 1999, Journal of Heat Transfer-Transactions of ASME, 121: 1011-1017
(Muley et al., 1999)
: dimensionless pump speed
: dimensionless impeller diameter
Flow rate ratio
Pressure ratio
: pressure ratio around the expander
Pressure drop
Pressure drop
Components Modeling
PEMFC-ORC Hybrid Power System

## Slide 12
Current density
(A/cm2)
Qgen
Qloss
1.0
0.9
0.8
0.7
Fig. (a) Total heat generation and heat loss of PEMFC stack (b) heat transferred by coolant with respect to operating cell temperature of PEMFC
(a)
(b)
Governing equations
Topping
PEMFC
Bottoming
ORC
Thermal Correlation of PEMFC
Results and Discussions

## Slide 13
Qcool,pemfc >> Qmax,evap (343~346 K at 1 A/cm2)
☞ Off-design operation appears
from the low temperature region
as increasing current density.
Cell temperature rise → Waste heat decreases
(Associated with thermal correlation of PEMFC)
Current density increases → Waste heat increases
Heat Input to the Bottoming ORC
Results and Discussions
Fig. Correlation of heat input and inlet temperature of hot fluid at the evaporator
Evaporator inlet temperature (K)

## Slide 14
Off-design
Current
density
(A/cm2)
Off-design
(a)
(b)
Low temperature condition restricts the bottoming ORC to achieve higher enhancement at the higher current density regions.
The waste heat → Refrigerant mass flow rate → Power & Efficiency
Evaporator inlet temperature (K)
Evaporator inlet temperature (K)
Performance of the Bottoming ORC
Results and Discussions
Fig. Performance correlation with heat source temperature in terms of (a) the expander’s power (b) the bottoming ORC’s thermal efficiency

## Slide 15
Hybrid
PEMFC
1.0
0.9
0.8
0.7
Current density
(A/cm2)
Hybrid
PEMFC
1.0
0.9
0.8
0.7
Current density
(A/cm2)
Fig. Performance comparison between hybrid system and PEMFC in terms of (a) power generation (b) energy efficiency
(a)
(b)
The hybrid systems has the optimal temperature at 353 K in power and efficiency.
The higher the current density, the bigger enhancement can be accomplished.
Performance Enhancement by the Bottoming ORC
Thermal Management for PEMFC

## Slide 16
The performance of the bottoming ORC
As the current density increases, the waste heat can exceed the capacity of the evaporator and cause off-design operation.
Performance enhancement by the bottoming ORC is more effective at the higher operating current density, the lower temperature.
The characteristics of waste heat from PEMFC
PEMFC generates more waste heat as it operate at higher current densities.
As the operating temperature increases, the amount of heat transferred by coolant decreases due to the rise of heat dissipation by sensible and latent heat.
The optimal performance of the hybrid power system
The suggested hybrid system has the best performance operating at 353 K in terms of both energy efficiency and power generation.
Considering the off-design operation, the current density are allowed to be increased until the evaporator can cover the amount of heat at the optimum temperature (353 K in this study).
Conclusion

## Slide 17
Thank you
Q & A